ADC STM32F3
Electrical Characteristics

---
STM32F3
- Each STM32F3 ADC is a 12-bit successive approximation ADC
- Each ADC has up to 18 multiplexed channels allowing the
  measurements of up to 16 external sources and up to 4 internal
  sources.
- A/D conversion can be performed in:
1) Single or multiple channels,
2) Discontinuous or continuous conversion mode,
3) Regular or injected mode,
4) Single or dual (simultaneous) mode

---
Conversion voltage range
- Min: 0V
- Max: Vref+
1. VREF+ is between 2 to VDDA
2. VDDA = 2.0 to 3.6 V:
3. Four ADCs 0.20 μS (up to 39 channels) with
4. selectable resolution of 12/10/8/6 bits, 0 to
5. 3.6 V conversion range, single
6. ended/differential input, separate analog supply
7. from 2 to 3.6

---
ADC Analog Power Supply
- Min: 2v Max:3.6v
2. Maximum current consumption at best performance:
Min: 907uA Max:1033uA

---
Sampling Frequency
Min: 0.14MHz Max: 72MHz
1. Sampling Rate:
4. For 12 bit:
5. Min: 0.01 *MSPS Max:5.14 MSPS
10. * Million Samples per second

---
ADC clock
The ADC clock is derived from the PLL output. It can reach 72 MHz and can be divided by the following prescalers values: 1,2,4,6,8,10,12,16,32,64,128 or 256. It is asynchronous to the AHB clock. Alternatively, the ADC clock can be derived from the AHB clock of the ADC bus interface, divided by a programmable factor (1, 2 or 4).